## Slide 1
Verifying an AXI4-to-APB bridge
UVM verification environment, directed-test phase
UVM 1.2 | Synopsys VCS | 14 directed tests
AXI4 master
agent
axi2apb
DUT
APB slave
agent
The bridge under test sits between two UVM agents
Notes: Introduce the project: a UVM environment that verifies the axi2apb bridge. The DUT is an AXI slave on one side and an APB master on the other, so the testbench plays AXI master and APB slave.
<number>

## Slide 2
Project goal and scope
14
directed tests
2
UVM agents: AXI and APB
7
RTL files under test
0
changes made to the DUT
What we verify
The axi2apb bridge: AXI4 slave port in, APB master port out. The supplied RTL stays unmodified.
How we verify
A dual-agent UVM environment: AXI master agent, reactive APB slave agent, scoreboard and coverage.
This phase
Directed tests first. Each test targets one behaviour of the bridge. Assertions come in a later phase.
<number>
Notes: Scope: one DUT, two agents, directed tests only. Seven RTL files are verified unmodified. The testbench-only fifo model is not counted.
<number>

## Slide 3
The DUT: axi2apb bridge
DUT: axi2apb
AXI master
(testbench)
Drives AW, W and AR.
Accepts B and R.
Channel buffers
5 x FIFO
AW, W, AR, R and B slices, depth 4 by default.
FSM
5 states
One transfer at a time. Read has priority over write.
APB master port
(DUT output)
PSEL fixed at 1. PENABLE marks an active request.
APB slave
(testbench)
Answers with PREADY, PRDATA and PSLVERR.
<number>
Notes: Walk left to right. The testbench plays both outer blocks. Inside the dashed boundary: five channel buffers (each a FIFO slice), the FSM, and the APB master port. Mention the missing fifo module and that it was reported rather than silently fixed.
<number>

## Slide 4
What the RTL actually does
PSEL fixed at 1
PENABLE rises with the request. There is no separate APB setup phase.
PSLVERR ignored
BRESP and RRESP are always OKAY, whatever the APB slave returns.
WSTRB and WLAST unused
The full WDATA word goes out on PWDATA, with no byte masking.
Read priority
If a read and a write are both pending, the read is served first.
Single beat only
AWLEN and ARLEN are not used, so bursts are not implemented.
Latch in the FSM
The always_comb block leaves NS unassigned in some branches.
<number>
Notes: These six observations come from reading the RTL. Each one is either checked by the scoreboard or documented by a dedicated test: PSLVERR and WSTRB have their own tests, read priority has the priority test.
<number>

## Slide 5
FSM: one transfer at a time
Read path
Dashed state: visited only when PREADY is low
IDLE
ARVALID wins and PENABLE rises
WAIT_R_PREADY
Only when PREADY is low
DONE_SINGLE_RD
RVALID into the R buffer
IDLE
Ready for the next request
Write path
IDLE
Needs AWVALID and WVALID
WAIT_W_PREADY
Only when PREADY is low
SEND_B_RESP
BVALID into the B buffer
IDLE
Ready for the next request
<number>
Notes: Two lanes, one per direction. The dashed wait states are only entered when PREADY is low in the first cycle. DONE_SINGLE_RD and SEND_B_RESP push the response into the R or B buffer and pop the request FIFOs.
<number>

## Slide 6
UVM environment architecture
Test + virtual sequence
UVM environment
AXI master agent
Sequencer
Driver with 5 channel engines
Monitor
APB slave agent
Sequencer for responses
Reactive driver
Monitor
DUT
axi2apb
Scoreboard: expected vs actual
Functional coverage
Monitors feed both
<number>
Notes: The test starts a virtual sequence. It drives the AXI sequencer and queues response items for the APB sequencer. Both monitors publish transactions to the scoreboard and the coverage collector.
<number>

## Slide 7
Project structure
axi2apb_uvm/
|-- build.flist
|-- Makefile
|-- rtl/ DUT + fifo model
|-- tb/ interfaces, tb_top
|-- uvm/ agents, env, scoreboard,
| coverage
|-- sequences/ AXI, APB, virtual
`-- tests/ 14 directed tests
One package
All UVM classes live in axi2apb_pkg and are included in a fixed order.
Plain interfaces
axi_if and apb_if use no clocking blocks or modports. Drivers use the negedge and monitors the posedge.
One build list
build.flist fixes the compile order: RTL, interfaces, package, then tb_top.
<number>
Notes: Folder layout follows the project specification: rtl, tb, uvm, sequences, tests. Assertions are deliberately left out of this phase.
<number>

## Slide 8
AXI agent: the master driver
axi_sequencer
axi_driver
dispatch
AW
W
AR
B
R
drive requests
collect responses
Negedge drive, posedge sample
Handshakes are detected on the rising edge, so no transfer is ever counted twice.
Channels run in parallel
AW, W and AR can be valid in the same cycle. The priority test depends on this.
One objection per item
Each item holds the phase open until its B or R response arrives, so a test never ends early.
<number>
Notes: The driver has one engine per channel. That is what lets AW, W and AR go valid together. Using objections per item means the run phase cannot finish while a response is still outstanding.
<number>

## Slide 9
APB agent: a reactive slave
Example with two wait states
cycle 1
cycle 2
cycle 3
cycle 4
PENABLE
PREADY
transfer completes
PREADY low, then high
PREADY stays low for two cycles while PENABLE is high, then goes high. The driver reacts on the negedge of the first PENABLE cycle, so zero wait states completes in one cycle.
Response items
The sequencer supplies wait cycles, PSLVERR and PRDATA for each transfer through try_next_item().
Memory model fallback
With no item queued, defaults and a memory model answer. Writes are stored and reads return the stored word.
End-to-end read-back
Because PRDATA comes from memory, a write followed by a read checks the whole path.
<number>
Notes: The DUT checks PREADY in the same cycle it raises PENABLE, so the driver must answer on the negedge of the first request cycle. Response items come from the APB sequencer; when none are queued the driver uses config defaults.
<number>

## Slide 10
Scoreboard: expected vs actual
Write: AXI to APB
Read: APB to AXI
Check | Expected | Actual
Address | AWADDR (AXI monitor) | PADDR (APB monitor)
Data | WDATA (AXI monitor) | PWDATA (APB monitor)
Response | OKAY (RTL behaviour) | BRESP
ID / USER | AWID, AWUSER | BID, BUSER
Check | Expected | Actual
Address | ARADDR (AXI monitor) | PADDR (APB monitor)
Data | PRDATA (APB monitor) | RDATA (AXI monitor)
Response | OKAY, RLAST = 1 | RRESP, RLAST
ID / USER | ARID, ARUSER | RID, RUSER
Timing checks too. The APB transfer must start after the AXI request was accepted, and the B or R response must come after the APB transfer completed. Expected values come from the other monitor or from documented RTL behaviour, never from the driver.
<number>
Notes: Expected values do not come from the driver. For writes the AXI monitor is the reference and the APB monitor is the actual. For reads it flips: the APB monitor's PRDATA is the reference for the RDATA seen by the AXI master.
<number>

## Slide 11
14 directed tests
1
Smoke
Idle check after reset, write then read-back
2
Single write
PREADY immediate, read-back check
3
Single read
Preloaded and forced PRDATA
4
Write wait states
PREADY low for 0 to 10 cycles
5
Read wait states
Same sweep for reads
6
RREADY delay
Back-pressure on the R channel
7
BREADY delay
Back-pressure on the B channel
8
9
Back-to-back reads
Eight pipelined reads
10
Back-to-back writes
Eight writes, then read-back
11
Mixed traffic
Writes and reads, varied waits
12
ID and USER
Propagation to B and R
13
PSLVERR
Documents that it is ignored
14
WSTRB
Documents the full-word write
<number>
Notes: Every test is a base test plus one virtual sequence. Number 8, the read/write priority test, is highlighted because the next slide walks through it.
<number>

## Slide 12
Deep dive: read vs write priority
1
Dispatch together
The vseq sends the write and the read with wait_resp = 0, so neither waits for the other.
2
Valid in the same cycle
The AW, W and AR engines all raise VALID on the same negedge.
3
One posedge, three pushes
All three handshakes finish on one edge and fill their FIFOs.
4
FSM picks the read
ARVALID is tested first, so the APB read runs before the write.
IDLE state in axi2apb.sv (simplified)
if (ARVALID) // read wins
start APB read
else if (AWVALID) // write if no read
start APB write
APB bus order seen by the scoreboard
1st: READ 0x500
2nd: WRITE 0x504
The test fails if the order is WRITE then READ.
<number>
Notes: Why wait_resp = 0 matters: if the write finished first, the read would never compete with it and the test would prove nothing. The pass criterion is the order of transfers recorded by the scoreboard.
<number>

## Slide 13
Build and run flow
build.flist
compile order
make compile
VCS builds one simv
make sim
one test, one seed
make regress
all tests, summary, coverage
Commands
make compile
make sim TEST=axi2apb_smoke_test
make sim TEST=axi2apb_rw_priority_test SEED=7
make regress # 14 tests + summary
make cov # urg coverage report
Pass or fail in the log
Each log ends with TEST PASSED or TEST FAILED.
One build, many runs
The same simv runs every test. Change SEED for another seed.
Coverage
VCS code coverage plus functional covergroups, merged by urg.
<number>
Notes: The Makefile follows the reference style but builds once and runs every test from the same simv. The regress target prints a PASS/FAIL table and then generates the merged coverage report.
<number>